## Slide 1: Computer Networks (Graduate level)
University of Tehran
Dept. of EE and Computer Engineering
By:
Dr. Nasser Yazdani
Lecture 6: Router & Switch Design

## Slide 2: Routers
How do you build a router
How to process and forward packets
Switch fabric design.
Assigned reading
  [P+98] A 50 Gb/s IP Router
  Chapter 3 of the book

## Slide 3: Outline
What is a router?
Router Architecture
  Different router Architectures
  The evolution of router architecture.
A case Study

## Slide 4: What is Routing?
A
B
C
R1
R2
R3
R4
D
E
F
R5

## Slide 5: Points of Presence (POPs)
A
B
C
POP1
POP3
POP2
POP4
D
E
F
POP5
POP6
POP7
POP8

## Slide 6: High Performance Routers Usage
R10
R11
R4
R13
R9
R5
R2
R1
R6
R3
R7
R12
R16
R15
R14
R8
(2.5 Gb/s)
(2.5 Gb/s)
(2.5 Gb/s)
(2.5 Gb/s)

## Slide 7: What a Router Looks Like
Cisco GSR 12416
Juniper M160
6ft
19”
2ft
Capacity: 160Gb/s Power: 4.2kW
3ft
2.5ft
19”
Capacity: 80Gb/s Power: 2.6kW

## Slide 8: IP Router
Router implements the following functionalities
  Forward packet to corresponding output interface, Forwarding engine.
  Manage routing/congestion
.
.
.
.
.
.

## Slide 9: Components of an IP Router
Control Plane
Datapath
per-packet
processing
Switching
Forwarding
Table
Routing
Table
Routing
Protocols
Two distinguish functional planes
Slow path or Control Plane
Fast Path or Data Plane

## Slide 10: Per-packet processing
Accept packet arriving on an incoming link.
Lookup packet destination address in the forwarding table, to identify outgoing port(s).
Manipulate packet header: e.g., decrement TTL, update header checksum.
Send packet to the outgoing port(s).
Buffer packet in the queue.
Transmit packet onto outgoing link.

## Slide 11: Generic Network Processor
Lookup
IP Address
Update
Header
Header Processing
Data
Hdr
Data
Hdr
~1M prefixes
Off-chip DRAM
Address
Table
IP Address
Next Hop
Queue
Packet
Buffer
Memory
~1M packets
Off-chip DRAM
Processing View

## Slide 12: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Data
Hdr
Data
Hdr
Data
Hdr
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr
Switching
Backplane
Central
Processor

## Slide 13: Function division
Line cards
  Network interface cards
Input interfaces:
  May enqueue packets and perform scheduling
Output interfaces:
  May enqueue packets and perform scheduling
Forwarding engine
  Fast path routing (hardware vs. software)
Backplane
  Switch or bus interconnect
Network controller or central unit
  Handles routing protocols, error conditions

## Slide 14: Router Architectures
Where to queue incoming packets?
Output queued
Input queued
Combined Input-Output queued
It is the same as switch architecture

## Slide 15: Output Router
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr
1
2
N
1
2
N
N times line rate
N times line rate

## Slide 16: Output Queuing (OQ)
Only output interfaces store packets
Advantages
  Easy to design algorithms: only one congestion point
Disadvantages
  Requires an output speedup of N, where N is the number of interfaces  not feasible
input interface
output interface
Backplane
C
RO

## Slide 17: Input Router
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr
1
2
N
1
2
N
Data
Hdr
Data
Hdr
Data
Hdr
Scheduler

## Slide 18: Input Queuing
Chart: Load
 | 0.72414 | 0.75439 | 0.78571 | 0.81818 | 0.85185 | 0.88679 | 0.92308 | 0.96078 | 1 | 1.0408 | 1.0833 | 1.1277 | 1.1739 | 1.2222 | 1.2727 | 1.3256 | 1.381 | 1.439 | 1.5 | 1.5641 | 1.6316 | 1.7027 | 1.7778 | 1.8571 | 1.9412 | 2.0303 | 2.125 | 2.2258 | 2.3333 | 2.4483 | 2.5714 | 2.7037 | 2.8462 | 3 | 3.1667 | 3.3478 | 3.5455 | 3.7619 | 4 | 4.2632 | 4.5556 | 4.8824 | 5.25 | 5.6667 | 6.1429 | 6.6923 | 7.3333 | 8.0909 | 9 | 10.1111 | 11.5 | 13.2857 | 15.6667 | 19 | 24 | 32.3333 | 49 | 99
The best that any queueing system can achieve.

## Slide 19: Input Queuing Head of Line Blocking
Chart: Load
 | 0.72414 | 0.75439 | 0.78571 | 0.81818 | 0.85185 | 0.88679 | 0.92308 | 0.96078 | 1 | 1.0408 | 1.0833 | 1.1277 | 1.1739 | 1.2222 | 1.2727 | 1.3256 | 1.381 | 1.439 | 1.5 | 1.5641 | 1.6316 | 1.7027 | 1.7778 | 1.8571 | 1.9412 | 2.0303 | 2.125 | 2.2258 | 2.3333 | 2.4483 | 2.5714 | 2.7037 | 2.8462 | 3 | 3.1667 | 3.3478 | 3.5455 | 3.7619 | 4 | 4.2632 | 4.5556 | 4.8824 | 5.25 | 5.6667 | 6.1429 | 6.6923 | 7.3333 | 8.0909 | 9 | 10.1111 | 11.5 | 13.2857 | 15.6667 | 19 | 24 | 32.3333 | 49 | 99
The best that any queueing system can achieve.

## Slide 20: Head of Line Blocking

## Slide 21: An input-queued (IQ) switch
R
R
1
R
R
R
R
R
R
2
3
N
…
Properties of an IQ switch
All buffering takes place at the input.
Input queues only need to be able to write packets at rate R (instead of N x R).
Consequences
Can build a switch N times faster.
But, a packet can be held up by packet ahead destined to a different output.
Hence an IQ switch is not “work conserving”. It can unnecessarily idle.
May not achieve “100% throughput”.
Average delay is not minimized.

## Slide 22: Input Queueing (IQ)
Advantages
  Easy to built
    Store packets at inputs if contention at outputs
  Relatively easy algorithm
    Only one congestion point, but not output…
    need to implement backpressure
input interface
output interface
Backplane
C
RO
Disadvantages
  Hard to achieve %100 utilization (due to output contention, head-of-line blocking)
    However, theoretical and simulation results show that for realistic traffic an input/output speedup of 2 is enough to achieve utilizations close to 1

## Slide 23: Virtual Output Queues

## Slide 24: with Virtual Output Queues
Chart: Load
 | 0.72414 | 0.75439 | 0.78571 | 0.81818 | 0.85185 | 0.88679 | 0.92308 | 0.96078 | 1 | 1.0408 | 1.0833 | 1.1277 | 1.1739 | 1.2222 | 1.2727 | 1.3256 | 1.381 | 1.439 | 1.5 | 1.5641 | 1.6316 | 1.7027 | 1.7778 | 1.8571 | 1.9412 | 2.0303 | 2.125 | 2.2258 | 2.3333 | 2.4483 | 2.5714 | 2.7037 | 2.8462 | 3 | 3.1667 | 3.3478 | 3.5455 | 3.7619 | 4 | 4.2632 | 4.5556 | 4.8824 | 5.25 | 5.6667 | 6.1429 | 6.6923 | 7.3333 | 8.0909 | 9 | 10.1111 | 11.5 | 13.2857 | 15.6667 | 19 | 24 | 32.3333 | 49 | 99
The best that any queueing system can achieve.

## Slide 25: Maximum Weight Matching
A1(n)
N
N
LNN(n)
A1N(n)
A11(n)
L11(n)
1
1
AN(n)
ANN(n)
AN1(n)
D1(n)
DN(n)
L11(n)
LN1(n)
“Request” Graph
Bipartite Match
S*(n)
Maximum
Weight Match

## Slide 26: Combined Input-Output Queueing (CIOQ) Routers
Both input and output store packets
Advantages
  Easy to achieve higher performance
    Utilization 1 can be achieved with limited input/output speedup (<= 2)
Disadvantages
  Harder design algorithms
    Two congestion points
    Need to design flow control
  Note: recent results show that with a input/output speedup of 2, a CIOQ can emulate any work-conserving OQ [G+98,SZ98]
input interface
output interface
Backplane
C
RO

## Slide 27: Generic Architecture of a High Speed Router Today
Combined Input-Output Queued Architecture
  Input/output speedup <= 2
Input interface
  Perform packet forwarding (and classification)
Output interface
  Perform packet (classification and) scheduling
Backplane
  Point-to-point (switched) bus; speedup N
  Schedule packet transfer from input to output

## Slide 28: Backplane
Point-to-point switch allows to simultaneously transfer a packet between any two disjoint pairs of input-output interfaces
Goal: come-up with a schedule that
  Meet flow QoS requirements
  Maximize router throughput
Challenges:
  Address head-of-line blocking at inputs
  Resolve input/output speedups contention
  Avoid packet dropping at output if possible
Note: packets are fragmented in fix sized cells (why?) at inputs and reassembled at outputs
  In Partridge et al, a cell is 64 B (what are the trade-offs?)

## Slide 29: Cell transfer
Schedule:
  Ideally: find the maximum number of input-output pairs:
    Resolve input/output contentions
    Avoid packet drops at outputs
    Packets meet their time constraints (e.g., deadlines), if any
Example
  Assign cell preferences at inputs, e.g., their position in the input queue
  Assign cell preferences at outputs, e.g., based on packet deadlines, or the order in which cells would depart in a OQ
  Match inputs and outputs based on their preferences
Problem:
  Achieving a high quality matching complex, i.e., hard to do in constant time

## Slide 30: Bus-Based Switches
Input Port Processors (IPP) do:
  lookup, sync and format conversion and put cells on bus
Output Port Processors (OPP)
  Buffer cells awaiting transmission
Control Processor (CP)
  exchanges control messages with terminals and other CPs
  configures connections by writing in IPP routing tables
Common bus interconnects various components.
  Requires bandwidth equal to sum of external link bandwidths;
  bus width must increase with number of links (scale?)
    capacitive loading generally reduces clock rate as number of links grows
Problems?
  Scale? Usually O(n2)
  OPP should operate with the rate of bus.
  Fairness?
CP
IPP
OPP
. . .
. . .

## Slide 31: Bus Arbitration: Rotating Daisy Chain (Fairness)
In systems where link bandwidth is larger than bus bandwidth, need mechanism to regulate bus access
Rotating token eliminates positional favoritism of static daisy chain
Not always fair
  if two consecutive inputs are competing “second” one gets fewer bus cycles
For “fair-sharing”
  advance token to winning IPP
Limited functionality!
0
request
data
request
data
request
data
request
data
1
0
0

## Slide 32: Bus Arbitration: Central Arbiter
ARB
request
data
request
data
request
data
request
data
IPPs send requests to central arbiter which picks winner.
Requests may include priority.
  static “importance” of data to be sent
  waiting time of data
  length of IPP queue
  combination
Arbiter can become a performance bottleneck.
Distributed version eliminates bottleneck
  uses bit-serial maximum computation to select highest priority value

## Slide 33: Two Level Bus Design(scale)
In simple bus, every driver and receiver contributes to capacitive loading.
  increases rise and fall times of signals, limiting frequency.
In two level bus, lower capacitive loads per segment.
Adds control complication and delay.
Can be extended to more than two levels, but diminishing returns.
. . .
Group Bus
Group Bus
Global Bus
Inputs from IPPs
Outputs to OPPs
. . .

## Slide 34: Subdivided Bus with Knockout Concentrators
Split bus into n “minibuses” with w/n wires each
Each minibus driven by just one IPP.
  cuts capacitive loading in half
  adding fanout components allows higher clock frequencies
OPPs concentrate n minibuses onto L<n outputs (optional)
OPPs must each be able to buffer up to L cells in parallel
Parallel reception complicates control somewhat
Concentration reduces required OPP memory bandwidth
IPP
IPP
IPP
IPP
w
w/n
OPPs

## Slide 35: Knockout Switch
Concentrator
  select l of
  n packets
Complexity: o(n2)
D
1
2
3
4
Outputs
Inputs
D
D
D
D
D
D
D
D
D
D
D
D
D

## Slide 36: Ring Switches
Ring Interfaces (RI) connect IPP and OPP to ring.
Ring avoids capacitive loading of bus, allowing higher clock frequencies.
Latency of 1-4 clock ticks per RI.
Same overall bandwidth requirements and complexity characteristics as bus.
Common control mechanisms
  token passing
  slotted ring with busy bit
  delay-insertion
ITI
RI
OTI
ITI
RI
OTI
ITI
RI
OTI
ITI
RI
OTI

## Slide 37: Shared Buffer Switches
Size of Memory can be estimated by taking the convolution of the queue length distributions of individual output queues.
For switches with 10 or more links, can reduce required memory by up to an order of magnitude.
Depends on independence of queuing processes at different outputs.
Queues are rarely full, then, memory for queues is rarely fully used.
Share memory among all queues.
Requires a central memory with bandwidth equal to twice the external link bandwidth. Bus bandwidth must also be doubled.
Per output or per flow queues typically implemented as linked lists.
CP
IPP
OPP
. . .
. . .
. . .

## Slide 38: Crossbar Switches
Crossbar allows multiple cells to pass in parallel to distinct outputs
  use of point-to-point transmission cuts capacitive loading at circuit board level
  parallelism allows smaller data path widths at IPPs, OPPs
Control circuit arbitrates access to outputs
  for each output can use any standard bus arbitration mechanism
    daisy-chain with optional rotating starting point
    dynamic priority arbitration mechanism
  alternative approach is time-slotted arbitration ring
Retains quadratic complexity, but concentrates it within chip or chip set, reducing impact on system cost
Controller
IPP
IPP
IPP
OPP
OPP
OPP
. . .
. . .

## Slide 39: Crossbar Implementation
Control
Detail of one column
IPPs
OPPs
a2a2 a1a1 a0a0
_ _ _
Control registers specify connected input.
Crosspoints decode specified “row number”.
New values are pre-loaded into staging registers.
One input can connect to multiple outputs.
control registers
staging registers

## Slide 40: Time Slotted Arbitration Ring
For each input, there is a register xi containing desired output, a register yi and a flip flop zi, linked in circular shift register; initially yi =i, zi=0.
Shift register shifts between each arbitration step, so yi , zi are assigned previous values of yi+1, zi+1.
During arbitration step, xi and yi are compared; if equal and if zi =0, then waiting cell has “won” and zi is set.
Make accessibility even by initializing yi to i+offset at start of each cycle, where offset is incremented by 1 modulo n before first step.
Arbitration time is proportional to n.
3
1
5
1
3
5
0
0
0
0
0
0
0
1
2
3
4
5
step 1
ü
ü
û
ü
û
û
y
z
1
1
0
2
0
3
0
4
1
5
0
0
step 2
y
z
0
2
0
3
0
4
1
5
0
0
1
1
step 3
y
z
x
0
3
0
4
1
5
0
0
1
1
0
2
step 4
y
z
0
4
1
5
0
0
1
1
0
2
1
3
step 5
y
z
1
5
0
0
1
1
0
2
1
3
0
4
step 6
y
z
positive acks

## Slide 41: Scalable Crossbar Controller
i,j
reqi
acki,j
rowi
requestorj
availi,j
winneri,j
columnj
ini
reqi
acki
rowi
0,0
0,1
0,3
0,2
0,4
0,5
0,7
0,6
1,0
1,1
1,3
1,2
1,4
1,5
1,7
1,6
2,0
2,1
2,3
2,2
2,4
2,5
2,7
2,6
3,0
3,1
3,3
3,2
3,4
3,5
3,7
3,6
4,0
4,1
4,3
4,2
4,4
4,5
4,7
4,6
5,0
5,1
5,3
5,2
5,4
5,5
5,7
5,6
6,0
6,1
6,3
6,2
6,4
6,5
6,7
6,6
7,0
7,1
7,3
7,2
7,4
7,5
7,7
7,6
in0
in1
in3
in2
in4
in5
in7
in6
out0
out1
out2
out3
out4
out5
out6
out7
column0
column1
column2
column3
column4
column5
column6
column7
Inputs send requests bit-serially along rows.
Arbitration Elements compare request bits to column number bits.
One AE per column holds token for rotating daisy-chain arbitration.
Token passed to AE following winner at end of cycle.
Approximately 25 gate-equivalents per AE.
  64 port crossbar controller requires 100K gates

## Slide 42: Arbitration Element Details
D
Q
>C
D
Q
>C
i,j
reqi
acki,j
rowi
requestorj
availi-1,j
availi,j
winneri,j
winneri-1,j
columnj
init
compare
pass
Upper flip flop holds token for arbitration process.
  passed at end of cycle to AE following winner
  if no winner in previous cycle, stays in same location
Lower flip flop & associated gates implement serial comparator.
  flip flop initialized to 1 and cleared on first mismatched bit
Acknowledgement returned to input, after arbitration.
Input passes row number through enabled tri-state driver to output.

## Slide 43: Output Contention in Crossbars
Different inputs can compete for one output.
Can alleviate by increasing crossbar bandwidth
Simple analysis
  assume each crossbar input has cell with probability p, each input cell is independent and output addresses are equiprobable.
  for any given output, probability that i cells are addressed to it is
  on average, there are n(1-p/n)n » ne-p outputs for which there are no cells.
  so, out of expected pn input cells, » (1-e-p)n leave.
  for p=1, about .63n can leave, implying limit on usable crossbar capacity.
More precise analysis shows that for large n, maximum crossbar throughput closer to .58n cells per cycle.

## Slide 44: Crossbar, Virtual Output Queues
Separate virtual output queues at each input.
  queues implemented using linked lists in common memory
Controller seeks to match inputs to outputs.
  keep outputs busy
  emulate queuing behavior of “ideal switch”
  best algorithms work well for arbitrary input traffic
  some speedup still needed
Does not extend readily to multicast.
  cannot associate cell with single VOQ
Controller
IPP
IPP
IPP
OPP
OPP
OPP
. . .
. . .
. . .

## Slide 45: Iterative Matching with Random Selection
outputs select inputs
traffic pairs
inputs select outputs
outputs select inputs
inputs select outputs
While there is an “unscheduled output” with waiting cells,
  for each unscheduled output with waiting cells, randomly select an input with cells to send
  for each selected input, randomly pick one of the selecting outputs
    call these (input,output) pairs, matched pairs
May produce as few as half the ideal number of matched pairs.
first round
second round

## Slide 46: Performance on Random Traffic
Ratio of number of “lost” transmit opportunities to input load
Negligible lost link capacity for speedups >1.5
Loss drops at heavy loads, since output queues rarely empty.

## Slide 47: Iterative Round Robin with iSLIP
i-SLIP algorithm seeks to desynchronize priorities.
  update priorities only for those outputs whose selections are “confirmed” in second half of round
  update priorities only in first round
  provides good performance for random traffic with minimal speedup
  works well even with limit on iterations
first round
second round
inputs select outputs
initial configuration
outputs select inputs
outputs select inputs
inputs select outputs

## Slide 48: High Performance Crossbars
Need parallelism for high performance systems.
  3210G system needs total bandwidth over 1 Tb/s
  single ICs now limited to under under 100 Gb/s
    32 gigabit serial links at 2.5 Gb/s each
“Bit-sliced” design makes best use of IC bandwidth.
IPP
OPP
crossbar chip
IPP
OPP
controller
  mux/demux convert single fast datapath to/from many small ones
    divides each cell into smaller pieces, or
    send each cell through just one crossbar - allows control to be parallelized too, but may get cells out of order
Can also build large crossbars by tiling smaller components.
  leads to complex and high cost systems (relative to alternatives)
  often done, but almost never a good idea

## Slide 49
Route
Table
CPU
Buffer
Memory
Line
Interface
MAC
Line
Interface
MAC
Line
Interface
MAC
Typically <20 Gb/s aggregate capacity
First Generation Routers
Shared Backplane
Line Interface
CPU
Memory

## Slide 50
Second Generation Routers
Route
Table
CPU
Line
Card
Buffer
Memory
Line
Card
MAC
Buffer
Memory
Line
Card
MAC
Buffer
Memory
Fwding
Cache
Fwding
Cache
Fwding
Cache
MAC
Buffer
Memory
Typically < 120 Gb/s aggregate capacity

## Slide 51
Third Generation Routers
Line
Card
MAC
Local
Buffer
Memory
CPU
Card
Line
Card
MAC
Local
Buffer
Memory
Switched Backplane
Line Interface
CPU
Memory
Fwding
Table
Routing
Table
Fwding
Table
Typically < 640 Gb/s aggregate capacity

## Slide 52
Fourth Generation Routers/Switches Optics inside a router for the first time
Switch Core
Linecards
Optical links
100s
of metres
0.3 - 10Tb/s routers in development

## Slide 53: A Case Study [Part., ’98]
Goal: show that routers can keep pace with improvements of transmission link bandwidths
Architecture
  A CIOQ router
  15 (input/output) line cards: C = 2.4 Gbps
    Each input card can handle up to 16 (input/output) interfaces
    Separate forward engines (FEs) to perform routing
  Backplane: Point-to-point (switched) bus, capacity B = 50 Gbps (32 MPPS)
    B/C = 20, but 25% of B lost to overhead (control) traffic

## Slide 54: Router Architecture
packet
header

## Slide 55: Architecture
1
15
input interface
output interfaces
Backplane
forward engines
Network
processor
Data in
Data out
Control data
(e.g., routing)
Update
routing
tables
Set scheduling
(QoS) state

## Slide 56: Data Plane
Line cards
  Input processing: can handle input links up to 2.4 Gbps (3.3 Gbps including overhead)
  Output processing: use a 52 MHz FPGA; implements QoS
Forward engine:
  415-MHz DEC Alpha 21164 processor, three level cache to store recent routes
    Up to 12,000 routes in second level cache (96 kB); ~ 95% hit rate
    Entire routing table in tertiary cache (16 MB divided in two banks)

## Slide 57: Control Plane
Network processor: 233-MHz 21064 Alpha running NetBSD 1.1
  Update routing
  Manage link status
  Implement reservation
Backplane Allocator: implemented by an FPGA
  Schedule transfers between input/output interfaces

## Slide 58: Checksum
Takes too much time to verify checksum
  Requires 17 instructions with min of 14 cycles, Increases forwarding time by 21%
Take an optimistic approach: just incrementally update it
  Safe operation: if checksum was correct it remain correct
  If checksum bad, it will be anyway caught by end-host
Note: IPv6 does not include a header checksum anyway!

## Slide 59: Slow Path Processing
Headers whose destination misses in the cache
Headers with errors
Headers with IP options
Datagrams that require fragmentation
Multicast datagrams
  Requires multicast routing which is based on source address and inbound link as well
  Requires multiple copies of header to be sent to different line cards

## Slide 60: Backplane Allocator
Time divided in epochs
  An epoch consists of 16 ticks of data clock (8 allocation clocks)
Transfer unit: 64 B (8 data click ticks)
During one epoch, up to 15 simultaneous transfers in an epoch
  One transfer: two transfer units (128 B of data + 176 auxiliary bits)
Minimum of 4 epochs to schedule and complete a transfer but scheduling is pipelined.
  Source card signals that it has data to send to the destination card
  Switch allocator schedules transfer
  Source and destination cards are notified and told to configure themselves
  Transfer takes place
Flow control through inhibit pins

## Slide 61: The Switch Allocator Card
Takes connection requests from function cards
Takes inhibit requests from destination cards
Computes a transfer configuration for each epoch
15X15 = 225 possible pairings with 15! Patterns

## Slide 62: Allocator Algorithm

## Slide 63: The Switch Allocator
Disadvantages of the simple allocator
  Unfair: there is a preference for low-numbered sources
  Requires evaluating 225 positions per epoch, which is too fast for an FPGA
Solution to unfairness problem: Random shuffling of sources and destinations
Solution to timing problem: Parallel evaluation of multiple locations
Priority to requests from forwarding engines over line cards to avoid header contention on line cards

## Slide 64: But…
Remember that if you want per flow processing the performance need to increase at a faster rate than the link capacity!
If link capacity increases by n, two effects:
  The time to process a packet decreases by n
  The number of flows increase (by n?), thus the per packet processing also increases

## Slide 65: Challenges
Build an optimal allocator that makes decisions in constant time
Packet classification.
Packet scheduling.

## Slide 66: Fast path of the code
Stage 1:
  Basic error checking to see if header is from a IP datagram
  Confirm packet/header lengths are reasonable
  Confirm that IP header has no options
  Compute hash offset into route cache and load the route
  Start loading of next header

## Slide 67: Fast path of the code
Stage 2
  Check if cached route matches destination of the datagram
  If not then do an extended lookup in the route table in Bcache
  Update TTL and CHECKSUM fields
Stage 3
  Put updated TTL, checksum and the route information into IP hdr along with link layer info from the forwarding table

## Slide 68: Some datagrams not handled in fast path
Headers whose destination misses in the cache
Headers with errors
Headers with IP options
Datagrams that require fragmentation
Multicast datagrams
  Requires multicast routing which is based on source address and inbound link as well
  Requires multiple copies of header to be sent to different line cards

## Slide 69: Instruction set
27% of them do bit, byte or word manipulation due to extraction of various fields from headers
The above instructions can only be done in E0, resulting in contention (checksum verifying)
Floating point instructions account for 12% but do not have any impact on performance as they only set SNMP values and can be interleaved
There is a minimum of loads(6) and stores(4)

## Slide 70: Issues in forwarding design
Why not use an ASIC in place of the engine ?
  Since IP protocol is stable, why not do it ?
  Answer depends on where the router will be deployed: corporate LAN or ISP’s backbone?
How effective is a route cache ?
  A full route lookup is 5 times more expensive than a cache hit. So we need modest hit rates.
  And modest hit rates seem to be assured because of packet trains

## Slide 71: Abstract link layer header
Designed to keep the forwarding engine and its code simple

## Slide 72: Forwarding Engine (P+88)
General purpose processor + software
8KB L1 Icache
  Holds full forwarding code
96KB L2 cache
  Forwarding table cache
16MB L3 cache
  Full forwarding table x 2 - double buffered for updates

## Slide 73: Network Processor
Runs routing protocol and downloads forwarding table to forwarding engines
  Two forwarding tables per engine to allow easy switchover
Performs “slow” path processing
  Handles ICMP error messages
  Handles IP option processing

## Slide 74: Line Card Interconnect (P+88)
Virtual output buffering
  Maintain per output buffer at input
  Solves head of line blocking problem
  Each of MxN input buffer places bid for output
Crossbar connect
Challenge: map of bids to schedule for crossbar

## Slide 75: Switch Scheduling (P+88)
Schedule for 128 byte slots
  Greedy mapping of inputs to outputs
Fairness
  Order of greedy matching permuted randomly
  Priority given to forwarding engine in schedule (why?)
Parallelized
  Check independent paths simultaneously

## Slide 76: Summary: Design Decisions (Innovations)
Each FE has a complete set of the routing tables
A switched fabric is used instead of the traditional shared bus
FEs are on boards distinct from the line cards
Use of an abstract link layer header
Include QoS processing in the router

## Slide 77: Why Faster Routers?
To prevent routers becoming the bottleneck in the Internet.
To increase POP capacity, and to reduce their cost, size and power.

## Slide 78: Why Faster Routers? 1: To prevent routers from being the bottleneck
Chart: Spec95Int CPU results
| 33909 | 34516 | 34516 | 34669 | 34669 | 34759 | 34881 | 34973 | 35065 | 35125 | 35125 | 35217 | 35309 | 35339 | 35339 | 35431 | 35462 | 35643 | 35735 | 35886 | 35886 | 36100 | 36100 | 36373 | 36434 | 36495 | 36678 | 36800 | 36892
Baseline | 2.15 | 3.66 | 4.24 | 2.45 | 3.45 | 4.25 | 5.96 | 8.08 | 7.08 | 4.31 | 8.82 | 9.77 | 11.2 | 9.82 | 12.6 | 12.3 | 12.1 | 16.3 | 16.5 | 9.33 | 12.4 | 24.1 | 25.9 | 33.2 | 34.7 | 35.5 | 36.8 | 30.9 | 44.6
0,1
1
10
100
1000
10000
1985
1990
1995
2000
Fiber Capacity (Gbit/s)
TDM
DWDM
Packet processing Power
Link Speed
2x / 18 months
2x / 7 months
Source: SPEC95Int & David Miller, Stanford.

## Slide 79: Why Faster Routers? 2: To reduce cost, power & complexity of POPs
POP with smaller routers
POP with large routers
  Ports: Price >$100k, Power > 400W.
  It is common for 50-60% of ports to be for interconnection.

## Slide 80: Fast Routers Difficulties?
It’s hard to keep up with Moore’s Law:
  The bottleneck is memory speed.
  Memory speed is not keeping up with Moore’s Law.
1.1x / 18 months

## Slide 81: Fast Routers Difficulties? Speed of Commercial DRAM
Chart: Access Time (ns)
| 1980 | 1983 | 1986 | 1989 | 1992 | 1995 | 1998 | 2001
Access Times | 150 | 120 | 100 | 80 | 60 | 50 | 45 | 40
Moore | 150 | 37.5 | 9.375 | 2.3 | 0.586 | 0.1465 | 0.0366 | 0.0092
Moore’s Law
2x / 18 months

## Slide 82: Fast Routers Difficulties?
It’s hard to keep up with Moore’s Law:
  The bottleneck is memory speed.
  Memory speed is not keeping up with Moore’s Law.
Moore’s Law is too slow:
  Routers need to improve faster than Moore’s Law.

## Slide 83: Router Performance Exceeds Moore’s Law
Growth in capacity of commercial routers:
  Capacity 1992 ~ 2Gb/s
  Capacity 1995 ~ 10Gb/s
  Capacity 1998 ~ 40Gb/s
  Capacity 2001 ~ 160Gb/s
  Capacity 2003 ~ 640Gb/s
Average growth rate: 2x / 18 months.

## Slide 84: Conclusions
It is feasible to implement IP routers at very high speeds
Today:
  Input link: 100 Gbps
  Backplane: 4 Tbps

## Slide 85: Next-lecture: software define Networking
What is SDN?
Why wee need SDN?
SDN Architecture.
Problems with SDN.